## Slide 1
VoIP: Voice over Internet Protocol for Small Single-board Computers
Trupesh Patel,
David Coleman,
Xiaoming Guo
{trpatel2, dmcoleman1, xguo29}@crimson.ua.edu
Term Project Presentation
April 27, 2022
Dr. Xiaoyan Hong
hxy@cs.ua.edu

## Slide 2: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 3: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 4: Objective
Modern telephone services are split between using traditional telephone networks and IP networks, such as the Internet. Voice over IP (VoIP) uses IP networks to make telephone calls, but it requires a machine running IP-PBX software to connect devices together for calls. A Raspberry Pi, a cheap and energy efficient single board computer, can run IP-PBX software and control calls made over VoIP, but it is limited by its low memory and weak CPU.
An examination has been performed to see how well the Raspberry Pi fulfills its IP-PBX functions with a variety of stressors, with the goal of determining the suitability of Raspberry Pis for IP-PBX software.
These tests were performed by running IP-PBX software on a Raspberry Pi, with calls made at different distances from the device and with the device working with different network difficulties.

## Slide 5: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 6: Introduction & Background: PBX & VoIP
Private Branch Exchange (PBX) is a technology which allows telephones to call each other, forwarding audio and controlling call behavior. While other technologies can provide similar services, PBX technology is designed for calls within a private institution.
With the advent of the internet, Voice over IP (VoIP) was created, allowing for telephone services to be provided over IP networks instead of standard telephone networks. Today, IP networks are so cheap and widespread that it is more cost efficient to use them for telephony than standard phone networks.
Hosting communication within a limited area, while still maintaining access to the entities outside is a natural characteristics of IoT scenarios and the reason IP-based PBX paradigm is suitable for IoT.

## Slide 7: Introduction & Background: IP-PBX
IP-PBX was made to act as a PBX for VoIP services, as a traditional PBX does not interact with IP networks.
IP-PBX is vital for IP telephony services, as without it, no two VoIP callers can connect to each other. IP-PBX can handle SIP messaging to manage call setup and RTP packages to relay audio data between callers and callees.
SIP and RTP/RTCP act as the backbone of IP-PBX.
SIP allows for calls to be started, connecting different callers together and allowing for complex behaviors such as putting callers on hold.
RTP/RTCP allows for an effective means of forwarding audio data between callers and the control of this forwarding.

## Slide 8: Introduction & Background: SIP
Provides the fundamentals of the PBX communication
In IP-based PBX implemented in the local network, the two proxy servers may merge into one.
SIP components:
  Model: session or pager
  Format: request/status line, header, body
From the SIP perspective, point out the core factors for a multimedia session: id, authentication, proxy, distance/hop count
Standard SIP

## Slide 9: Introduction & Background: RTP/RTCP
  RTP carries the media streams, while RTCP is used to monitor transmission statistics and quality of service
  RTP: sensitive to packet delays and less sensitive to packet loss
  Elements for RTP: sequence number, timestamp, source identifier, contributor identifier for multiple source
  RTCP allows the recipients so that they can send feedback to the source or sources.

## Slide 10: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 11: Obstacles
PBX is complex
  The IP-PBX software used was Asterisk PBX, a very robust and mature implementation, making it also very complicated
  Much third party software is involved: Asterisk PBX for the PBX, Zoiper to make calls, Wireshark for packet capture, SIP.US for SIP trunking, etc.
Raspberry Pis could not initially access Eduroam without a large amount of additional setup

## Slide 12: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 13: Analytical Method
Primary metrics to be analyzed are loss and jitter.

## Slide 14: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 15: Experiments
There were two primary methods for testing the functionality of the Raspberry Pi.
  Make calls at a variety of locations of different distance from the Raspberry Pi
    In the same room
    On the same floor
    In the same building

## Slide 16: Expectation at Final Submission

## Slide 17: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 18: Future Direction

## Slide 19: Content
Objective
Introduction & Background
Obstacles
Analytical Method
Experiments
Future Directions
Conclusion

## Slide 20: Conculsion

## Slide 21: Special Thank You!

## Slide 22: Any Questions?